## Slide 1: Reliability Applications Series, Parallel, Series-Parallel and Non-Series Parallel
ECE 313
Probability with Engineering Application
Professor Ravi K. Iyer
University of Illinois

## Slide 2: Today’s Topics
Quick Review series, parallel, series-parallel and non-series parallel
m-out-of-n-systems
  Special Case Triple Modular Redundancy

## Slide 3: Application to Reliability Evaluation of Series, Parallel, Series-Parallel Systems
Consider the problem of computing reliability of so-called series-parallel systems.
A series system is one in which all components are so interrelated that the entire system will fail if any one of its components fails.
A parallel system is one that will fail only if all its components fail.
We will assume that failure events of components in a system are mutually independent. Consider a series system of n components.

## Slide 4: Application to Reliability Evaluation (cont.)
For I=1,2,…,n, define events Ai=“Component i is functioning properly.” The reliability, Ri, of component i is defined as the probability that the component is functioning properly. Then: Ri=P(Ai).
By the assumption of series connections, the system reliability:
(2.1)
(“The system is functioning properly.”)

## Slide 5: Example of Effect of Complexity on Reliability
Remember how quickly system reliability degrades with an increase in complexity.
For example, if a system consists of five components in a series, each having a reliability of 0.970, then the system reliability is 0.9705=0.859.
If the system complexity is increased so that it contains ten similar components, its reliability is reduced 0.97010=0.738.
Consider what happens to system reliability when a large system such as a computer system consists of tens to hundreds of thousands of components.

## Slide 6: Increasing Reliability Using Parallel Redundancy
One way to increase the reliability of a system is to use redundancy, i.e., to replicate components with small reliabilities. This is called parallel redundancy.
Consider a system consisting of n independent components in parallel; the system fails to function only if n components have failed.
Define event Ai=“The component i is functioning properly” and
Ap=“The parallel system of n components is functioning properly.”
Also let Ri=P(Ai) and Rp=P(Ap).
To establish a relation between Ap and the Ai’s, it is easier to consider the complementary events.
Thus: “The parallel system has failed.”
= “All n components have failed.”
Therefore, by independence:

## Slide 7: Increasing Reliability Using Redundancy (cont.)
Now let Fp=1-Rp be the unreliability of the parallel system, and similarly let Fi=1-Ri be the unreliability of component i.
Then, since Ai and Ai are mutually exclusive and collectively exhaustive events, we have:
And:
Then:
And:

## Slide 8: Product Law of Unreliabilities
Thus, for parallel systems of n independent components, we have a product law of unreliabilities analogous to the product law of reliabilities of series systems.
If we have a parallel system of five components, each with a reliability of 0.970, then the system reliability is increased to:
However, we should be aware of the law of diminishing returns.

## Slide 9: Reliability Curve of a Parallel Redundant System
1.0
0.99
0.98
0.97
0.96
0.95
Reliability Rp(n)
Number of components n, each with R=0.97
1.0 2.0 3.0 4.0 5.0 6.0 7.0 8.0 9.0 10.0

## Slide 10: Reliability of Series-Parallel Systems
We can use formulas parallel and series systems in combination to compute the reliability of a system having both series and parallel parts (series-parallel systems).
Consider a series-parallel system of n serial stages, where stage i consists of ni identical components in parallel.

## Slide 11: Reliability of Series-Parallel Systems (cont.)
The reliability of each component of stage i is Ri.
Assuming that all components are independent, Rsp :

## Slide 12: Series-Parallel System Example
Consider the series-parallel system shown in the diagram below, consisting of five stages, with n1=n2=n5=1, n3=3, n4=2, and R1=0.95, R2=0.99, R3=0.70, R4=0.75, and R5=0.9.
Then:
R1
R2
R3
R3
R3
R4
R4
R5

## Slide 13: Application of Bayes Complex system Example
Consider evaluating the reliability R of the five-component system. The system is said to be functioning properly only if all the components on at least one path from point A to point B are functioning properly.
C1
C2
C3
C4
C5
A
B

## Slide 14: Bayes’ Formula Example 3 (cont.)
Define for i = 1, 2, …, 5 event Xi = “Component i is functioning properly”
  let Ri = reliability of component i = P(Xi)
  let X = “System is functioning properly
  let R = system reliability = P(X)
Thus X is a union of four events
These four events are not mutually exclusive. Therefore, we cannot directly use axiom (A3). Note, however, that we could use relation (Rd), which does apply to union of interesting events. But this method is computationally tedious for a relatively long list of events. Instead, using the theorem of total probability, we have:

## Slide 15: Bayes’ Formula Example 3 (cont.)
Now to compute P(X|X2)observe that since component C2 is functioning, the status of components C1 and C3 is irrelevant. The system is equivalent to two components C4 and C5 in parallel. Therefore we get:
To compute P(X|X2), since C2 is known to have failed, the resulting system is a series-parallel one whose reliability is:
Combining previous equations and substituting, we have:

## Slide 16: ZJUI Lecture Non-Series parallel and Triple Modular Redundancy
Another Non Series-Parallel example
Bernoulli Trials
  An application of Bernoulli trials: Triple Modular redundancy - TMR
Announcements:
  HW 3 on Thursday and due the following Thursday 11:59pm

## Slide 17: Reliability of Series-Parallel Systems
summary
Expressions for parallel and series systems and in combination to compute the reliability and failure probabilities (series-parallel systems).
Application of conditional probability to resolve a non-series parallel system example

## Slide 18: Non-Series Parallel System Example
B
A
C
D
E
F
B (“ short ”) works
A
E
F
C
D
B (“ open ”) fails
B Working
B Not Working
Rsys = RB P(system works | B works) + (1 - RB) {RD[1 - (1 - RARE)(1 - RFRC)]}

## Slide 19: Non-Series-Parallel-Systems (cont.)
A
D
E
B (“ short ”) works, C (“ short ”) works
F
A
D
B (“ short ”) works, C (“ open ”) fails
Reduction with B and C replaced
P(system works | B works) = RC{RD[1 - (1 - RA)(1 - RF)]} + (1 - RC)(RARDRE)
Letting RA ....RF = Rm yields Rsys = R6m - 3R5m + R4m + 2R3m
A
C
D
E
F
B (“ short ”) works
B Working

## Slide 20: Non-Series Parallel System Example
A Working

## Slide 21: Non-Series Parallel System Example
A Not Working

## Slide 22: Non-Series Parallel System Example

## Slide 23: Next: Bernoulli Trials and application to a TMR system
Bernoulli Trials
Triple Modular Redundant Systems

## Slide 24: Bernoulli Trials
Physical situations of interest:
1. Observe n consecutive executions of an if statement, with success = “then clause is executed” and failure =”else clause is executed”
2. Examine components produced on an assembly line, with success = “acceptable” and failure = “defective”
3. Transmit binary digits through a communication channel, with success = “digit received correctly” and failure = “digit received incorrectly”

## Slide 25: Bernoulli Trials (cont.)
4. Consider a time-sharing computer system that allocates a finite quantum (or time slice) to a job scheduled for processor service. Observe n time-slice terminations, with success = “job has completed processing” and failure = “job still requires processing and joins the tail end of the ready queue of processes
CPU
Job completion
Job arrival
Ready queue

## Slide 26: Bernoulli Trials (Cont’d)
Consider a random experiment that has two possible outcomes,. Let the probabilities of the two outcomes be p and q, respectively, with p + q = 1.
Now consider the compound experiment: A sequence of n independent repetitions of this experiment. Such a sequence is a sequence of Bernoulli trials.

## Slide 27: Bernoulli Trials (cont.)
Let 0 denote failure and 1 denote success. Let Sn be the sample space of an experiment involving n Bernoulli trials, defined by:
  S1 = {0, 1}, S2 = {(0, 0), (0, 1), (1, 0), (1, 1)}
  Sn = {2n n-tuples of 0’s and 1’s}.
The probability assignment over the sample space S1 is already specified: P(0) = q  1, P(1) = p  1, and p + q = 1. We wish to assign probabilities to the points in Sn.
Let Ai = “Success on trial i” and Ai = “Failure on trial i” then P(Ai) = p and P(Ai) = q.

## Slide 28: Bernoulli Trials (cont.)
Consider s an element of Sn such that s = (1, 1, …, 1, 0, 0, …, 0) [k 1’s and (n-k) 0’s]. Then the elementary event {s} can be written:

## Slide 29: Bernoulli Trials (cont.)
Therefore:
Similarly, any sample point with k 1’s and (n-k) 0’s is assigned probability pkqn-k. Noting that there are such points, the probability of obtaining exactly k successes in n trials is :
Verify that expression for P(s) is a legitimate probability assignment over the sample space Sn since
by the Binomial theorem.
k = 0, 1, …, n

## Slide 30: Example
Consider a binary communication channel transmitting coded words of n bits each. Assume that the probability of successful transmission of a single bit is p (and the probability of an error is q = 1-p), and the code is capable of correcting up to e (e >=0) errors.
For example, if no coding or parity checking is used, then e = 0. If a single error correcting Hamming code is used then e =1.
If we assume that the transmission of successive bits is independent, then the probability of successful word transmission is:

## Slide 31: Bernoulli Trials Example m-out-of-n system
Consider a system with n components that requires m (£n) or more components to function for the correct operation of the system (called m-out-of-n system).
If we let m=n, then we have a series system; if we let m = 1, then we have a system with parallel redundancy.
Assume: n components are statistically identical and function independently of each other.
Let R denote the reliability of a component ( and q = 1 - R gives its unreliability), then the experiment of observing the status of n components can be thought of as a sequence of n Bernoulli trials with the probability of success equal R.

## Slide 32: Bernoulli Trials Example (cont.)
Now the reliability of the system is:
It is easy to verify that:

## Slide 33: Bernoulli Trials TMR System Example
As special case of m-out-of-n system, consider a system with triple modular redundancy (TMR). In such a system there are three components, two of which are required to be in working order for the system to function properly (i.e., n = 3 and m = 2). This is achieved by feeding the outputs of the three components into a majority voter.
R
R
R
Voter
Output
Input
Triple-triple redundant 777 primary flight computer
IEEE Xplore
https://ieeexplore.ieee.org › document
by YC Yeh · 1996 · Cited by 451 — The heart of the FB concept is the use of triple redundancy for all hardware resources: computing system, airplane electrical power, hydraulic power ….

## Slide 34: Bernoulli Trials TMR System Example (cont.)
The reliability of TMR system is given by the expression:
and thus Note that:
Thus TMR increases reliability over the simplex system only if the simplex reliability is greater than 0.5; otherwise decreases reliability
Note: the voter output corresponds to a majority; it is possible for two or more malfunctioning units to agree on an erroneous vote.

## Slide 35: Reliability of TMR vs. Simplex

## Slide 36: Reliability of TMR vs. Simplex